## Slide 1: Rethinking Remote Memory Placement on Large-Memory Systems with Path Diversity
Wonkyo Choe, Sang-Hoon Kim, Jeongseob Ahn
Ajou University
Notes: Hello, everyone. I am Wonkyo Choe and will be starting a Ph.D in the following Fall semester. This work is about a new memory placement on large-memory systems using multi-chip characteristics. The work is done with two advisors, Sang-Hoon Kim and Jeongseob Ahn. (Clxick)

## Slide 2: Emerging multi-chip systems
Data center utilizes multi-chip systems to build scale-up servers
  Memory controllers for each processor die
Chip manufacturers is developing such systems
  AMD EPYC
  Intel Xeon
Advanced point-to-point interconnect
  AMD Infinity Fabric (IF)
  Intel Ultra Path Interconnect (UPI)
Notes: The data centers build large-memory systems to handle a huge amount of data. For this purpose, they mainly use multi-chip systems, which refers to 4 or more processors not just dual chips. These systems usually have one or two memory controllers so they get a large amount of memory capacity.
With this trend, the major chip manufactures put an effort to develop a scalable processor. An example of this is EPYC chip from AMD and Xeon chip from Intel corporations.
The main benefit of those processors is an advanced technology, point-to-point interconnect which provides almost the same latency on remote access across the chips. Each vendor has different name of it: One is Infinity Fabric from AMD, the other is Ultra Path Interconnect from Intel.
First, let’s look at the characteristics of this interconnect in detail. (Click)

## Slide 3: A distinct feature of multi-chip systems
All remote memory access latencies are similar
  Local latency ~= 85 ns
  Remote latecny ~= 140 ns
If the latencies are not that different,
doesn’t it matter to allocate memory on any nodes?
Notes: This graph is a read latency of different processors. One with the thick blue color is Intel processor and the other with the pale thin marine blue color is AMD processor. For Intel processor, we use physical Intel Xeon processor and for AMD processor, we use AWS instance which uses 2.5 GHz AMD EPYC 7000 series processors. A X axis refers each NUMA node, and a Y axis refers latency.
In this graph, we can figure that the remote access latencies do not have significant gap with each other.
Due to this feature, we produce an idea like this (Click): If the latencies are not that different, doesn’t it matter to allocate memory on any nodes?
To check this in detail, we dig out how OS works to allocate memory. (Click)

## Slide 4: Traditional NUMA systems
Linux configures multi-chip systems as a cpu node
Each node has own memory node
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
Notes: In OS, especially Linux kernel, based on Intel Scalable processor, Linux consists of each physical chip as an abstract CPU node. We call it NUMA node. Like the square graphic, a CPU node represents a physical CPU and the below boxes represent a memory node. (Click)

## Slide 5: Default memory placement (first-touch)
local memory is not enough
  Linux requires memory from other memory nodes
  Fallback node list determined when system boots
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
Thread A
1
2
3
4
Thread B
1
2
4
3
Notes: In Linux, based on the previous node information, it gives pages to processes. The default mem policy is first-touch. This policy allows a process to use the local memory first and the rest of nodes will be used when the local memory ends. In other words, when the local memory is not enough memory, the kernel finds other node to provide the memory. In this process, the kernel uses fallback node list which is statically configured upon the boot.
For example, one application is running on CPU-0. (Click)
Considering the policy, the app uses the local memory (Click)
and then based on fallback node list, it allocates memory in the following order. Node 1 or DIMM-1 (Click)
DIMM-2 (Click)
And the last DIMM-3 (Click)
If the app stays in CPU-2. It uses the local memory based on the default policy.
Again, following the fallback node list, the kernel let the process use DIMM-3 memory
And then DIMM-0, Lastly, DIMM-1

## Slide 6: Default memory placement (first-touch)
Depends on where thread at
For instance, located at CPU-2
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
Thread A
1
2
3
4
Notes: If the app stays in CPU-2. It uses the local memory based on the default policy.
Again, following the fallback node list, the kernel let the process use DIMM-3 memory
And then DIMM-0, Lastly, DIMM-1

## Slide 7: Our insight
Existing systems do not exploit diverse memory path (path diversity)
  All remote latency is almost the same
  Static Linux’s fallback node list
Existing memory placement causes unintended interference
  Multiple applications would use the same memory node
Notes: With the previous insight: One is gained from interconnect technology of the multi-chip systems and the other one is from Linux fallback list; We found an opportunity to exploit those features for better performance and look for how we efficiently use multiple paths.
On top of that, we found another problem when multiple applications are running, and we concluded that memory interference hampers applications when they are using the same node.
Let’s see how it looks like (Click)

## Slide 8: Memory interference
For example, two applications are running
  App A uses DIMM-0 & DIMM-1
  App B uses DIMM-1
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
App A
App B
1. Memory Interference
2. Other memory idle
Notes: For brevity, assume that there are two memory intensive applications are running. App A is using over the local memory capacity and App B is using only the half of its local memory. In this scenario, we found two main problems which prevent apps from showing better performance.
(Click) The first one is memory interference. As it shows, due to the app A’s memory, App B cannot use enough memory bandwidth. On the other hand, App A is also experiencing performance drop because App B is currently using the DIMM-1 memory.
(Click) Second, other memory nodes are idle. Since Linux relies on the fallback list, it does not allocate memory even if others have enough.
With these two problem, we concluded that there should be a better memory placement to handle them. (Click)

## Slide 9: Our insight
Existing system not exploit diverse memory path
  Static Linux’s fallback node list
  All remote latency is almost the same
Existing memory placement causes unintended interference
  Multiple applications would use the same memory node
Hybrid & Usage-aware memory placement
Notes: In summary, from the first insight, exising system not exploit diverse memory path, and the second insight, the current memory placment causes memory interference. (Click)
We designed our simple memory placement techniques for the Linux kernel. We call it Hybrid and Usage-aware memory placement. (Click)

## Slide 10: Rest of the talk
Hybrid & Usage-aware memory placement
Performance evaluation
Discussion
Conclusion
Notes: For the rest of talk, I will introduce the design of each memory placement, and performance evaluation. Also, I will talk about our facing problems as discussion and will end with conclusion. (Click)

## Slide 11: Hybrid placement
First-touch (Linux default) + page-interleave (round-robin allocation)
  Use first-touch when allocating local memory
  Use page-interleave when allocating remote memory
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
App A
App B
App C
App D
Notes: First, let’s look at the hybrid memory placement. Hybrid memory placement is combination between exisiting first-touch and page-interleave policy.
I will introduce how it works. Before going into the design, note that our case is every node has only one application.
Let say, except for App A, other application uses only their own the local memory and their threads are also pinned on the local node.
App A is only the one that uses a large memory. Currently, App A takes all the local memory. So far, all applications are under the first-touch rule.
(Click) However, once App A tries to use the remote memory, interleaving policy is applied. That is, App A does not use the only single memory, but use the entire remote memory.
As applying this policy, it can reduce hotspot problem on App B which is occurred in the only default policy and distributes the memory traffic. (Click)

## Slide 12: Usage-aware placement
First-touch (Linux default) + usage-aware
  Use first-touch when allocating local memory
  Allocate memory based on memory usage (allocation on the least usage)
CPU-0
DIMM-0
CPU-1
DIMM-1
CPU-2
DIMM-2
CPU-3
DIMM-3
App A
App B
App C
App D
Notes: Usage-aware memory placement has a similar way with the hybrid placement. Like the hybrid, at first, all applications follow the default policy which allocates a memory from the local. However, for usage-aware memory, assume that App B and App D allocate more memory than App C. Therefore, the number of allocated pages on DIMM-2 is the least on the system.
(Click) At this time, if App A needs more memory and requires it from the remote memory, the kernel allows App A to allocate memory from the idlest node. In other words, the kernel only finds the least usage node across the remote memory. (Click)

## Slide 13: Implementation
Leverage the kernel data structure to know # of allocated pages
  struct pglist_data
  struct zone
The system counts # of allocated page on each process
  When a process uses beyond the local memory, the proposed policies applied
Counted pages include active & inactive pages
Notes: To implement the proposed polices, we leverage the kernel data structure to obtain the number of allocated pages and how many free pages are left.
The information is included in two data structures: struct pglist_data, struct zone. The first data structure contains the information of a single node. The second data structure represents multiple zones in each node.
With these data structures, our system counts how many pages are left or allocated in each node. And then, based on the stats, the system applies our proposed policies.
These numbers include active and inactive pages no mattter a page is anonymous or file. (Click)

## Slide 14: How we set our environment
4 sockets machine
  Intel Xeon Gold 6242: A single chip (16 physical cores) on each socket
  16GB * 4 socket = total 64 GB memory capacity
Linux kernel v5.3
  AutoNUMA enabled
Benchmark
  Mcf / fotonik3d / cam4 from SPECCPU 2017
  MG from NAS parallel benchamrk
  GUPS from HPC Challenge benchmark
  Liblinear
Notes: To evaluate our design, we set up our system environment. Our system has 4 sockets and each socket has a single Intel processor.
Each socket has 16GB DRAM memory so the total memory capacity is 64GB.
We use Linux kernel version 5.3 and this default options are applied.
For benchmark, we mainly use memory intensive workloads. We evaluate various workloads from SPECCPU 2017, but in this talk we show only three workloads.
For NAS benchmark, we use MG and for HPC Challenge, we use GUPS, and lastly liblinear. (Click)

## Slide 15: Other consideration for evaluation
Memory intensive workload on CPU-0 spills memory
  Eventually uses the remote memory
  MG / GUPS / Liblinear
The rest of workloads on each CPU-X except CPU-0
  Use only the local memory
Various mixed sets are experimented
  Few results are included in the paper
Notes: For better evaluation, we set a few details on each experiment.
Applications on CPU-0 usually have the large-memory footprint so it tries to use the remote memory. MG, GUP, and Liblinear are the candidates.
The rest of applications only use the local memory; In other words, they have a small memory footprint, but memory-intensive workloads.
We evaluate various mixed for better evaluation, but in this paper, we only show a few of them. (Click)

## Slide 16: Performance comparison
First-touch (FT)
Page-interleave (PI)
  Allocate a page one by one on each node
  numactl
Hybrid (HY)
Usage-aware (UA)
Notes: In the following graph, there are 4 targets to compare each performance. First-touch / Page-interleave / Hybrid / usage-aware.
For page-interleave, a process uses all memory node one by one every time a page is allocated. (Click)

## Slide 17: Performance of Proposed polices
All proposed policies are improved over first-touch (FT)
Memory intensive workload (mg, liblinear, mcf) perf. Bounded memory bandwidth
Page-interleave(PI) impairs other workloads, such as cam4 due to memory interference
2
3
Notes: The graph is the result of performance evaluation. X axis indicates each node and application names. Y axis is normalized execution time so the lower is better. We use harmonic mean because we would like to see how much the system shows the overall improvement.
First, all policies we proposed are showing improved performance over the default policy. (Click)
Second, For page-interleave, the main reason is that the performance of memory intensive workloads, such as mg / liblinear, are bounded memory bandwidth. In other words, if they use the multiple remote memory node, they use the broaden memory bandwidth. (Click)
However, page-interleave impairs cam4 so the overall performance is dropped. (Click)

## Slide 18: Performance of Proposed polices
4. Not like PI, our proposed policies, Hybrid(HY) & Usage-aware(UA) not impair cam4
  Overall, harmonic mean has improved on our policies
4
Notes: On the other hand, unlike page-interleave, our proposed design does not hurt cam4 so much and at the same time, they acquires the overall improved performance. (Click)

## Slide 19: Memory allocation graph
For first-touch, mg significantly interferes with mcf
For page-interleave, all workloads interferes with each other
For Hybrid & Usage-aware, memory interference little on mcf
Notes: The previous figures can be explained by the allocation graph. The graph tells allocation status of each application upon time. First, the default policy causes hot-spot problem so mcf application is having trouble with making performance. Second, page-interleave intereferes with each other and it eventually hurts some of workloads’ performance. However, for our policy, we minimize hot-spot problme and interference. Finally, we achieve better performance. (Click)

## Slide 20: Discussion
Localizing data
  Increased remote accesses
  Hard for scheduler to minimize them
Applying policies to different typologies
  Policy on different NUMA group & NUMA distance
  Allocate closest neighbor group and then faraway group
Notes: For discussion, we are facing few issues for our design.
First, basically Linux tries to localize data. However, since our design increases remote accesses, the scheduler is having difficulty to minimize these accesses and try to find the best schedule. We are investigating this issue.
Second, in this work, our system consists of a single numa node in a single numa group. However, for other topologies such as AMD processors, the different number of NUMA domain and distance exists. Currently, our solution for this is to allocate closest neighbor group and then allocate faraway group. However, for generalization and the detail, we left it as our future work. (Click)

## Slide 21: Conclusion
Exploiting path diversity on multi-chip systems
Simple memory placement for multiple applications
  Hybrid & Usage-aware
Minimizing hot-spot or interference and show better performance.
Notes: To wrap up,
In this work, we show how to exploit path diverstiy on multi-chp systems by leveraging interconnet technology.
We design and show simple memory placement for multiple applications.
Lastly, we minimize hot-spot issue, memory interference and finally achieve the overall better performance.
Thank you for listening. Please ask any question and I would be happy to answer.